UPS Monitoring Software

\

UPSee N414

Quick Start

Compatible with

Microsoft Windows XP

Microsoft Windows 2000

Microsoft Windows ME

Microsoft Windows 98

1111 W. 35th Street Chicago, IL 60609 USA

Customer Support: (773) 869-1234 • www.tripplite.com

Copyright ©2005 Tripp Lite. All rights reserved. SmartOnline™ is a trademark of Tripp Lite.

COPYRIGHT ANNOUNCEMENT

LIMITED WARRANTY

THE PROGRAM AND ENCLOSED MATERIALS ARE PROVIDED “AS IS” WITHOUT WARRANTY OF ANY KIND, EITHER EXPRESSED OR IMPLIED, INCLUDING BUT NOT LIMITED TO THE IMPLIED WARRANTIES OF MERCHANT ABILITY. THE ENTIRE RISK AS TO QUALITY AND PERFORMANCE OF THE PROGRAM AND ENCLOSED MATERIAL IS ASSUMED BY YOU.

Index

◆Hardware Installation-----------------------------------4

◆Software Installation------------------------------------5

1. IPTool setting----------------------------------------6

2. Connect the NETCARD---------------------------6

3. Program Execution---------------------------------7

Please follow the instructions below to install the NETCARD into your UPS.

◆ For Hardware Installation：

Connect NETCARD with UPS & Internet.

□ Turn off the UPS.

□ Insert the NETCARD into the slot of the UPS.

□ Connect the NETCARD to LAN, using the RJ-45 port.

□ Switch on the UPS.

◆Software Installation：

Configure NETCARD IP Address

& Parameters

NETCARD Configuration Flow Chart

1. IPtool Setting

- Execute the IPtool program.

- Click on the “Search”icon, the program will start searching all NETCARDs on the Internet and display all searched NETCARDs on the windows browser.

- To start the NETCARD setting. Please click on the NETCARD on the browser list.

- After the modification, please click on the “Update” icon to modify the NETCARD.

- The user will receive the latest NETCARD parameters setting from the windows browser.

2.  Connect the NETCARD

- Upon completion of the NETCARD setting, the user will be able read the UPS real-time information every five seconds via windows Internet Explorer.

- Click on the ”UPS Information” to receive the UPS product information..

- For controlling the UPS and the WEB. Please click on the “UPS Control”. It will only allows ”Test 10 Seconds” and ”Turn On/Off Beep” on these 2 functions.

3. Program Execution：

A. “Start” -> “All Programs” -> UIS SOFT -> UPSeeN

Main Screen

Real-time display

B. Parameter Setting

UPS & IP configuration

UPS name：Name the UPS

IP address：NETCARD IP Address

Add：Add IP

Update：Update the record

Auto Scan：Search all NETCARD on the network and assign numbers for UPSes.

Completed UPS & IP configuration

- The upper part of the screen displays UPS NAME, IP, and VIN… information.

- The lower part of the screen will display the most recently 10 events. Otherwise, please click “Events record” for previous records.

# Text boxes

Connect NETCARD ,

UPS and Network

Use the IPtool to configure the Internet setting of the NETCARD.

Start the monitoring software (UPSee N) of NETCARD, in-order to receive the information on the NETCARD

To log-on to IP address, use the IE browser to connect the NETCARD

Simple System Diagram

System Status

Parameters

English